## Slide 1
EXCELLENCE
EXCELLENCE
CLASS 11 - 2026-27
CLASS 11 - 2026-27
Physics
Units 06
Units and Measurement
Easy Instruments: Scale, Vernier, Screw Gauge
By - Excellence Programme
19 October 2026
1
Notes: From PW Units and Measurement Lecture 08. Final Units lecture.

## Slide 2
What we learn today
01
Metre scale — the simple ruler
02
Vernier callipers — how to find least count
03
How to read a vernier
04
Zero error — when the instrument is wrong at zero
05
Screw gauge — for very small lengths
2

## Slide 3
CLASS NOTE
Link from last class
3
Last class we learned how error grows when we add, multiply or raise a number to a power. That part is done.
Today we learn the tools that measure length: a metre scale, vernier callipers and a screw gauge. The key word is least count — the smallest length the tool can measure.
Least count = smallest length the instrument can show
Class notes come after teaching. These slides are for the board.

## Slide 4
WORDS
Short names we will use
4
• L.C. = least count (smallest step the tool can show)
• M.S.D. = one small mark gap on the main scale
• V.S.D. = one small mark gap on the vernier scale
• M.S.R. = main scale reading | V.S.R. = vernier scale reading
Learn these four short names. Questions use them a lot.

## Slide 5
IDEA
Three tools for length
5
• Metre scale — a normal ruler with millimetre marks.
• Vernier callipers — a ruler plus a short sliding scale.
• Screw gauge — a screw tool for very thin objects.
All three measure length. Least count tells how fine the reading can be.

## Slide 6
ROUGH WORK
Rough work / extra work
6
Notes: Empty board for extra working.

## Slide 7
RULE
Metre scale
7
On a school metre scale, marks are 1 mm apart. So the smallest length you can read is 1 mm. That 1 mm is the least count.
Least count of metre scale = 1 mm
Write the answer as (reading ± 1 mm)
If a rod ends between 4 mm and 5 mm, write 4 mm ± 1 mm. Do not guess 4.2 mm.

## Slide 8
IDEA
Why we need a vernier
8
A metre scale cannot show lengths smaller than 1 mm. Vernier callipers fix that. They have a fixed main scale and a short scale that slides. That short scale is the vernier.
The vernier marks are a little closer than the main marks. So one vernier mark can line up exactly with a main mark. That helps us read a small part of 1 mm.
L.C. = 1 M.S.D. − 1 V.S.D.

## Slide 9
RULE
Easy school vernier
9
In school, 10 vernier marks match 9 main marks. Each main mark gap is 1 mm. So one vernier gap is a bit less than 1 mm.
10 V.S.D. = 9 mm → 1 V.S.D. = 0.9 mm
L.C. = 1 mm − 0.9 mm = 0.1 mm
If n vernier marks match (n − 1) main marks: L.C. = (1 M.S.D.) / n

## Slide 10
METHOD
Only two jobs
10
• Job 1: Find the least count from how the two scales match.
• Job 2: Find the reading = main reading + (vernier mark × least count).
Reading = M.S.R. + (V.S.R. × L.C.)
Write the final answer as (reading ± least count).

## Slide 11
QUESTION
Least count: 9 and 12
11
One main mark gap is 1 cm. 9 main gaps match 12 vernier gaps. Find the least count.

## Slide 12
ANSWER
Solution: Least count: 9 and 12
12
Idea: find one vernier gap, then subtract it from one main gap.
Step 1: 1 V.S.D. = (9/12) × 1 cm = 0.75 cm
Step 2: L.C. = 1 − 0.75 = 0.25 cm
Final answer: 0.25 cm

## Slide 13
ROUGH WORK
Rough work / extra work
13
Notes: Empty board for extra working.

## Slide 14
QUESTION
25 vernier marks
14
25 vernier marks match 24 main marks. One main mark gap is 1 mm. Least count is
1
0.04 mm
2
0.01 mm
3
0.02 mm
4
0.08 mm

## Slide 15
ANSWER
Solution: 25 vernier marks
15
Idea: use L.C. = 1 M.S.D. − 1 V.S.D.
Step 1: 1 V.S.D. = 24/25 mm = 0.96 mm
Step 2: L.C. = 1 − 0.96 = 0.04 mm
Final answer: 0.04 mm (option 1)

## Slide 16
QUESTION
Formula with x and n
16
One main mark gap is x cm. n vernier marks match (n − 1) main marks. Least count in cm is
1
(n − 1)x / n
2
n x / (n − 1)
3
x / n
4
x / (n − 1)

## Slide 17
ANSWER
Solution: Formula with x and n
17
Idea: this is the same school rule, written with letters.
Step 1: 1 V.S.D. = ((n − 1)/n) × x
Step 2: L.C. = x − ((n − 1)/n)x = x/n
Final answer: x / n (option 3)

## Slide 18
ROUGH WORK
Rough work / extra work
18
Notes: Empty board for extra working.

## Slide 19
QUESTION
20 vernier and 8 main
19
1 cm on the main scale is cut into 10 equal parts. 20 vernier marks match 8 of those small parts. Find least count.

## Slide 20
ANSWER
Solution: 20 vernier and 8 main
20
Idea: find 1 M.S.D., then 1 V.S.D., then subtract.
Step 1: 1 M.S.D. = 1/10 cm = 0.1 cm
Step 2: 1 V.S.D. = (8/20) × 0.1 = 0.04 cm
Step 3: L.C. = 0.1 − 0.04 = 0.06 cm
Final answer: 0.06 cm

## Slide 21
METHOD
How to read a vernier
21
Look at the zero mark of the vernier. The main mark just before it is the main scale reading. Then look for the vernier mark that lines up with any main mark. That number is the vernier reading.
Reading = M.S.R. + V.S.R. × L.C.
Example: 3 mm + 4 × 0.1 mm = 3.4 mm
Write it as (3.4 ± 0.1) mm

## Slide 22
IDEA
What is zero error?
22
Close the jaws with nothing inside. The two zero marks should meet. If they do not meet, the tool already shows a small wrong reading. That wrong reading is called zero error.
Always subtract the zero error from the reading you took. Keep the + or − sign. Zero correction is just the opposite of zero error.
True reading = reading you took − zero error

## Slide 23
RULE
Positive zero error
23
Jaws closed. If vernier zero is to the right of main zero, zero error is positive. Size = (matching vernier mark) × least count.
Zero error = + (matching vernier mark) × L.C.
Example: 4th mark matches, L.C. = 0.1 mm → zero error = +0.4 mm
Zero correction here is −0.4 mm. Error and correction have opposite signs.

## Slide 24
ROUGH WORK
Rough work / extra work
24
Notes: Empty board for extra working.

## Slide 25
RULE
Negative zero error
25
Jaws closed. If vernier zero is to the left of main zero, zero error is negative. For a 10-mark vernier, use (10 − matching mark) × least count, and put a minus sign.
Zero error = − (N − matching mark) × L.C.
Example: N = 10, 6th mark matches, L.C. = 0.1 mm → zero error = −0.4 mm
Minus a negative error means you add. True = reading + 0.4 mm

## Slide 26
QUESTION
Find zero correction
26
Jaws closed. Vernier zero is to the right of main zero. 5th vernier mark matches. L.C. = 0.1 mm. Zero correction is
1
0.4 mm
2
+0.5 mm
3
−0.5 mm
4
−0.4 mm

## Slide 27
ANSWER
Solution: Find zero correction
27
Idea: right side means + error. Correction flips the sign.
Step 1: Zero error = +5 × 0.1 = +0.5 mm
Step 2: Zero correction = −0.5 mm
Final answer: −0.5 mm (option 3)

## Slide 28
QUESTION
Fix a vernier reading
28
Zero error = +0.2 mm. Vernier zero is between 8.5 cm and 8.6 cm. Matching vernier mark = 6. L.C. = 0.01 cm. Correct length is
1
8.58 cm
2
8.54 cm
3
8.56 cm
4
8.36 cm

## Slide 29
ANSWER
Solution: Fix a vernier reading
29
Idea: use one unit. Change 0.2 mm to 0.02 cm.
Step 1: Reading taken = 8.5 + 6 × 0.01 = 8.56 cm
Step 2: True length = 8.56 − 0.02 = 8.54 cm
Final answer: 8.54 cm (option 2)

## Slide 30
ROUGH WORK
Rough work / extra work
30
Notes: Empty board for extra working.

## Slide 31
QUESTION
Sphere with zero error
31
1 M.S.D. = 0.1 cm. 10 vernier marks match 9 main marks. Jaws closed: 6th vernier mark matches (vernier zero is left). With sphere: M.S.R. = 3.1 cm, 1st vernier mark matches. Diameter is
1
3.07 cm
2
3.11 cm
3
3.15 cm
4
3.17 cm

## Slide 32
ANSWER
Solution: Sphere with zero error
32
Idea: least count → zero error → sphere reading → true value.
Step 1: L.C. = 0.1 / 10 = 0.01 cm
Step 2: Zero error = −(10 − 6) × 0.01 = −0.04 cm
Step 3: Reading taken = 3.1 + 1 × 0.01 = 3.11 cm
Step 4: True = 3.11 − (−0.04) = 3.15 cm
Final answer: 3.15 cm (option 3)

## Slide 33
QUESTION
Diameter of a cylinder
33
No zero error. Vernier zero is between 5.10 cm and 5.15 cm. 50 vernier marks = 2.45 cm. 24th vernier mark matches. Diameter is
1
5.112 cm
2
5.124 cm
3
5.136 cm
4
5.148 cm

## Slide 34
ANSWER
Solution: Diameter of a cylinder
34
Idea: gap 5.10 to 5.15 means 1 M.S.D. = 0.05 cm.
Step 1: 1 V.S.D. = 2.45 / 50 = 0.049 cm
Step 2: L.C. = 0.05 − 0.049 = 0.001 cm
Step 3: Diameter = 5.10 + 24 × 0.001 = 5.124 cm
Final answer: 5.124 cm (option 2)

## Slide 35
QUESTION
20 vernier match 16 main
35
Main scale marks are 1 mm apart. 20 vernier marks match 16 main marks. Least count is
1
0.02 mm
2
0.05 mm
3
0.1 mm
4
0.2 mm

## Slide 36
ANSWER
Solution: 20 vernier match 16 main
36
Idea: same subtract rule again.
Step 1: 1 V.S.D. = 16/20 = 0.8 mm
Step 2: L.C. = 1 − 0.8 = 0.2 mm
Final answer: 0.2 mm (option 4)

## Slide 37
ROUGH WORK
Rough work / extra work
37
Notes: Empty board for extra working.

## Slide 38
QUESTION
n marks in one centimetre
38
Main scale has n marks in 1 cm. n vernier marks match (n − 1) main marks. Least count is
1
1 / ((n + 1)(n − 1)) cm
2
1 / n cm
3
1 / n² cm
4
1 / (n(n + 1)) cm

## Slide 39
ANSWER
Solution: n marks in one centimetre
39
Idea: one main gap is already 1/n cm.
Step 1: 1 M.S.D. = 1/n cm
Step 2: L.C. = (1 M.S.D.) / n = 1/n² cm
Final answer: 1 / n² cm (option 3)

## Slide 40
QUESTION
Fill the blank
40
Vernier constant = 0.1 mm. Zero error = (−0.05) cm. M.S.R. = 1.7 cm. Matching vernier mark = 5. Correct diameter = ____ × 10−² cm.

## Slide 41
ANSWER
Solution: Fill the blank
41
Idea: change 0.1 mm to cm first, then find true length.
Step 1: L.C. = 0.1 mm = 0.01 cm
Step 2: Reading taken = 1.7 + 5 × 0.01 = 1.75 cm
Step 3: True = 1.75 − (−0.05) = 1.80 cm = 180 × 10−² cm
Final answer: 180

## Slide 42
ROUGH WORK
Rough work / extra work
42
Notes: Empty board for extra working.

## Slide 43
QUESTION
Least count in mm
43
One main mark gap is a cm. The nth vernier mark matches the (n − 1)th main mark. Least count in mm is
1
10 n a / (n − 1)
2
10 a / (n − 1)
3
10 a / n
4
(n − 1)a / (10 n)

## Slide 44
ANSWER
Solution: Least count in mm
44
Idea: in cm, L.C. = a/n. Times 10 gives mm.
Step 1: L.C. = a/n cm = 10a/n mm
Final answer: 10 a / n (option 3)

## Slide 45
IDEA
Screw gauge in plain words
45
A screw gauge is used for very small lengths, like the diameter of a thin wire. When you turn the screw once, it moves forward by a fixed length. That fixed length is called pitch.
Pitch = how far the screw moves in one full turn
L.C. = Pitch / (number of marks on the round scale)
Reading = linear reading + (round-scale mark × L.C.)

## Slide 46
RULE
Zero error of screw gauge
46
Close the ends with nothing between them. The zero of the round scale should meet the line. If it does not, there is a zero error — just like in the vernier.
True reading = reading you took − zero error
Screw gauge least count is smaller than vernier. That is why we use it for thin wires.

## Slide 47
QUESTION
Find the pitch
47
A screw gauge has least count 0.01 mm and 50 marks on the round scale. Pitch is
1
0.01 mm
2
0.25 mm
3
0.5 mm
4
1.0 mm

## Slide 48
ANSWER
Solution: Find the pitch
48
Idea: Pitch = least count × number of marks.
Step 1: Pitch = 0.01 × 50 = 0.5 mm
Final answer: 0.5 mm (option 3)

## Slide 49
ROUGH WORK
Rough work / extra work
49
Notes: Empty board for extra working.

## Slide 50
QUESTION
Wire diameter
50
Pitch = 0.5 mm. Round scale has 50 marks. Linear reading = 2.5 mm. Round reading = 20. Zero error = +0.02 mm. True diameter is

## Slide 51
ANSWER
Solution: Wire diameter
51
Idea: least count → reading taken → subtract zero error.
Step 1: L.C. = 0.5 / 50 = 0.01 mm
Step 2: Reading taken = 2.5 + 20 × 0.01 = 2.70 mm
Step 3: True = 2.70 − 0.02 = 2.68 mm
Final answer: 2.68 mm

## Slide 52
CLASS SUMMARY
Remember these lines
52
Metre scale least count = 1 mm
Vernier: L.C. = 1 M.S.D. − 1 V.S.D. (or 1 M.S.D. / n)
Reading = M.S.R. + V.S.R. × L.C.
True reading = reading taken − zero error
Screw gauge: L.C. = Pitch / N. Same zero-error rule.

## Slide 53
FOR THE EXAM
Four lines to write
53
1. Vernier least count = 1 M.S.D. − 1 V.S.D.
2. Reading taken = M.S.R. + (matching vernier mark × L.C.)
3. True reading = reading taken − zero error
4. Screw gauge least count = Pitch / (round marks)
These four lines are enough for most board questions.

## Slide 54
ROUGH WORK
Rough work / extra work
54
Notes: Empty board for extra working.

## Slide 55
PRACTICE
Try these at home
55
1. 50 vernier marks match 49 main marks. 1 M.S.D. = 1 mm. Find least count.
2. M.S.R. = 4.2 cm, V.S.R. = 7, L.C. = 0.01 cm, zero error = +0.03 cm. Find true length.
3. Pitch = 1 mm, round scale has 100 marks. Find least count in mm and in cm.
4. Ends closed. Round reading = −3, L.C. = 0.01 mm. Write zero error and zero correction.
Units chapter is finished. Next chapter: Motion in a Straight Line.